## Slide 2
MSG (Meteosat Second Generation)
Presentation
Syed Mustafa Haider
Space Division (Alpha 6)
RS and GIS (Intern)

## Slide 3: PRESENTATION OUTLINE
Introduction
  MSG
MSG Instruments
  Gerb
  SEVIRI
SEVIRI Channels
Meteosat Series Products
  MPEF products
  SAF Products
Extractable Features
Comparison with other satellites

## Slide 4: Introduction
The Meteosat satellites are operated as a two-satellite system providing detailed full disc imagery over Europe and Africa every 15 minutes and rapid scan imagery over Europe, every five minutes.
Meteosat imagery is crucial for nowcasting, which is about detecting rapidly developing high impact weather and predicting its evolution a few hours ahead, in support of the safety of life and property.
Meteosat satellites have been providing crucial data for weather forecasting since 1977.

## Slide 5: Meteosat Second Generation
MSG (Meteosat Second Generation) consists of a series of four geostationary meteorological satellites, along with ground-based infrastructure, that will operate consecutively until 2020.
The launch dates of Meteosat were:
MSG-1/Meteosat-8: 28 August 2002
MSG-2/Meteosat-9: 21 December 2005
MSG-3/Meteosat-10: 5 July 2012
MSG-4: Meteosat-11 15 July 2015
Notes: The time interval in which nadir point of the satellite passes over the same point on the Earth’s surface for a second time (when the satellite retraces its path) is called the repeat cycle of the satellite.

## Slide 6: MSG Instruments
The MSG has an image repeat cycle of 15 min, with 30 min for (Meteosat) having 12 spectral channels. MSG consists of 4 satellites MSG 1, 2, 3 and 4.
The primary instruments in the MSG series are the SEVIRI(Spinning Enhanced Visible and Infrared Imager) sensor and the GERB ( Geostationary Earth Radiation Budget) instrument.
GERB monitors the radiation budget in terms of climate change, food production and natural disaster prediction which is achieved by measuring the top layer of the atmosphere, the shortwave and emitted longwave of the region.
GERB includes two instruments the IOU (Instrument Optical Unit) imager device and the Instrument Electronics Unit (IEU) data handeling device.

## Slide 7: MSG Instruments: GERB
GERB monitors the radiation budget in terms of climate change, food production and natural disaster prediction which is achieved by measuring the top layer of the atmosphere, the shortwave and emitted longwave of the region.
GERB includes two instruments the IOU (Instrument Optical Unit) imager device and the Instrument Electronics Unit (IEU) data handeling device.

## Slide 8: MSG Instruments: SEVIRI
SEVIRI is an abbreviation for Spinning Enhanced Visible and Infrared Imager which in simpler terms has 12-channel imager observing the earth-atmosphere system, from which 11 channels observe the full disk of the earth with a 15-min repeat cycle.
The HRV (High resolution Visible) channel covers half of the full earth disk in the east to west direction and full disk in the north-south direction. The HRV has a spatial resolution of 1.67 km.

## Slide 9: SEVIRI Channel
The channel detail for SEVIRI are as follows:

## Slide 10: SEVIRI Channels
The basic use and working of the channels are as follows:
VIS 0.6 and VIS 0.8: These channels’ primary resource is cloud detection and tracking of cloud movement, aerosol monitoring along with land surface temperature and vegetation monitoring. These two channels are known from AVHRR of the NOAA polar orbiting satellite.
NIR 1.6: The primary resource of this channel is the ability to discriminate between snow and cloud cover, ice and water clouds and aerosol monitoring.
IR 3.9: The primary resources of this channel is low cloud and fog detection, supports measurement of land and sea surface temperature at night time, low level wind coverage from cloud tracking.

## Slide 11: SEVIRI Channels
WV 6.2 and WV7.3: The primary resources of these two channels are water vapor and wind observation.
IR 8.7: This channel provides quantitative information on cirrus clouds and assist the discrimination process between ice and water clouds.
IR 9.7: Tracking Ozone patterns that represent the wind motion in the lower stratosphere
IR 10.8 and IR 12.0: These two channels are split window channels, the primary resource these channel offer are measuring of sea, land surface and cloud-top temperatures along with assisting in the detection of cirrus and volcanic ash cloud.
IR 13.4: In cloud free areas/ clear sky cases it assists the calculation of temperature measurement from the lower troposphere.

## Slide 12: METEOSAT SERIES PRODUCTS
There are various products produced by the Meteosat series, the operational meteosat meteorological products are handled by the MPEF (Meterological Product Extraction Facility), the MTP (Meteosat transition program) products are specifically produced by the MPEF (the core products are wind products extracted from three channels in near-real time.
The current operational products are as follows:
CLA (Cloud analysis products): In simpler terms this product provides scene analysis results on a scale of 100 km x 100 km or better along with providing information on cloud cover, cloud-top temperature, cloud type and phase and assisting the generation of Atmospheric Motion Vectors (AMV) which can provide information on wind speed and direction.

## Slide 13: METEOSAT SERIES PRODUCTS
Cloud-top height (CTH): a derived product image which provides information regarding cloud height at a resolution of 3 x 3 super pixel resolution. Mainly used in aviation meteorology as it provides heights with a vertical resolution of 300m.
Clear-Sky radiance: This product provides the mean radiance of cloud free pixels in [W m−2 sr−1 (cm−1) −1]
Tropospheric humidity (TH): This product provides estimates of mean-relative humidity for two tropospheric layers.

## Slide 14: METEOSAT SERIES PRODUCTS
Atmospheric motion vectors: important for numerical weather prediction. This product would be derived from cloud and water vapor motion using primarily the 0.6- or 0.8-µm channel, the 10.8-µm channel, and the 6.2- and 7.3-µm channels.
ISCCP dataset (IDS): continues the support to the International Satellite Cloud Climatology Program (ISCCP) providing three different data formats.

## Slide 15: METEOSAT SERIES PRODUCTS
Climate dataset (CDS): provides statistical information about the scene classes in a processed segment (nominally 32 × 32 pixels). It is a concise summary of the radiances observed in a segment and potentially very useful for climatological studies of cloud and radiation fields.
Total ozone product (TOZ): This uses the 9.7-µm channel and other SEVIRI channels and correlative data, and is derived with a regression algorithm. The ozone observations are useful for monitoring and forecasting UV radiation at the ground level.

## Slide 16: Satellite Application Facilities (SAF) products
•Examples of products from the Ocean and Sea Ice SAF include
(i) Atlantic sea surface temperature,
(ii) surface radiative fluxes over the Atlantic,
• Examples of products from the Climate SAF are
(i) cloud parameters,
(ii) surface radiation budget components,
(iii) radiation budget components at the top of the atmosphere,
• Examples of targeted products from the Land Surface Analysis SAF are
(i) vegetation parameters and biophysical indicators,
(ii) snow cover,
(iii) land surface temperature,
(iv) soil moisture,

## Slide 17: Extractable Features
The following primary features can also be extracted from the MSG data,
Visible imagery: can be used for monitoring cloud cover, land cover and atmospheric conditions.
Infrared imagery: deals with capturing temperature variations in the earth’s surface and atmosphere. This can be used for monitoring cloud-top temperatures, identifying areas of precipitation and temperature data.

## Slide 18: Extractable Features
Water Vapor imagery: this corresponds to the collection of atmospheric moisture patterns and humidity variations.
Multispectral Imagery: refers to the creation of composite images that can be used in land-use classification and vegetation monitoring.
Derived Products: As the name implies these are products derived from satellite data such as sea surface temperatures, atmospheric motion vectors and etc. These products can be used in weather forecasting , climate monitoring and etc.
These datasets are often provided in standard formats such as NetCDF, HDF, or GeoTIFF. The specific format may depend on the data distribution policies of EUMETSAT or the organization providing access to the satellite data.

## Slide 19
LANDSAT | METEOSAT | SENTINEL | MODIS
program managed by the United States Geological Survey (USGS) and NASA. | part of the European Organization for the Exploitation of Meteorological Satellites (EUMETSAT) | part of the European Space Agency's (ESA) Copernicus program | sensor operating on the Terra and Aqua satellites, which were launched by NASA
designed for Earth observation and environmental monitoring. | primary purpose is meteorological observation, specifically monitoring and forecasting weather and climate patterns | designed for a variety of Earth observation purposes, including monitoring land, oceans, and the atmosphere. | designed to collect data on Earth's land, oceans, and atmosphere. provides a wide range of data, including imagery, land surface temperature, and atmospheric parameters
sun-synchronous polar orbit | geostationary orbit | Various orbits, including polar orbits for global coverage and geostationary orbits for specific tasks | sun-synchronous polar orbits
records data for a given spot on the Earth every 18 days | records every half hour a circular disk of the earth surface covering mostly Africa and Europe. | Record data every 10 days with the first spacecraft, reducing to every 5 days once both are in orbit. | Record data every 1 to 2 days
Landsat satellites have multiple spectral bands, including visible, near-infrared, short-wave infrared, and thermal infrared. | Meteosat satellites primarily capture data in the infrared and visible light spectrum. | Different Sentinel satellites have various spectral bands and resolutions | Wide range of spectral bands covering visible, infrared, and thermal wavelengths with moderate spatial resolution.